## Slide 1: Inside the Machine
Amod Malviya
Notes: First half - overview, 2nd half - deeper

## Slide 2: Mindset & Principles
Reasoning >> facts
Thinking is mandatory!
We cannot reason without asking questions. So question!
I will lie!
I will lie only about “facts”, not about “method of reasoning”.
You cannot counter with a looked-up fact. Only reasoning.

## Slide 3: Why understand internals?

## Slide 4
Webserver
50%
compute
50%
network + disk
Perf increase?
40%
60%
1.8x
1.56x
10x

## Slide 5: Amdahl’s Law
Max gain possible is always constrained by the unchanged part
Law of diminishing returns
(of improving only one part)
You’re always chasing the next bottleneck
(which there are many)
improvement -> ∞
Notes: Assignment: In the 40-60 scenario, what amount of CPU improvement will lead to 80% of max gains possible?

## Slide 6: Why understand internals?
Understand the bottlenecks - we cannot improve what we do not understand
Good engineering requires good/innovative use of resources
Gives a lens to understanding a large number of programs
Get better at tech support for friends & family
Notes: Databases, Redis, OS, Network, Distributed Systems

## Slide 7: High Level Overview

## Slide 8
Asus Z790 mobo
VRM
Memory
CPU Socket
Ports
Chipset
PCIe x16 slots
PCIe slots
SATA & M.2
Notes: How many can we identify?
How do we characterize each one of them?

## Slide 9
CPU
NVMe SSD
SATA Disk
GPU
PCIe card
USB
Ethernet
Memory
I/O
async ifc
(mostly)
sync ifc
(mostly)
What’s the difference ?!
Connectivity?
Notes: Difference b/w IO vs Mem – slow/fast? privilege? async?
  Q: What’s common between all I/O devices?
  Q: Why *should* mem be sync? (Assignment)
  Q: Why *should* IO mostly be async? Unbounded behaviour.
Either better CPU/IO/Mem, or the connectivity

## Slide 10: Computer Performance is mostly architecting Compute, Memory, I/O & Connectivity
Hardware
AND
Software
Latency & Throughput

## Slide 11
5 pooris max
(bandwidth: 5ppm)
Throughput helps hide latency
Latency/order
Throughput
1 m
AvgLat/order
Throughput
2 ppm
1 m
2 ppm
2
Orders (poori)
Customer
Stall
Utilization
40%
1 m, 2m
2 ppm, 3 ppm
1.5 m
2.5 ppm
2
50%
Throughput’s only purpose is to
hide latency
only if designed to do so
1 min fry-time
+ 3
1 m, 1 m
2 ppm, 3 ppm
1 m
5 ppm
100%
2
+ 3
?
?
?
?
7 + 10
?
Notes: Q: Can throughput hide latency without limit?
Q: Other examples? Git commit, traffic, network, OS
Assignment: Complete the 7+10 example
Assignment: 3 examples of latency hiding via throughput (other than ones discussed)
Assignment: latency hiding via throughput in HTTP server

## Slide 12
CPU
Chipset
NVMe SSD
SATA Disk
GPU
4x 100Gbps PCIe NIC
USB
Ethernet
Memory
DDR
x16 lanes
x4 lanes
x4 lanes
DMI / UMI
PCIe 1x lane = 16 Gbps (PCIe 4.0)
100+ns
0.1ns
25 GB/s
50 ns
1Gbps
10-100us
3 GB/s
2-10 ms
150 MB/s
Lies?
Notes: Compute vs Mem vs IO bound
Q: Should the CPU directly support multiple kinds of IO?
Q: Is DMI part of the 20 lanes? Or in addition?
Q: Why is GPU connected to direct PCIe lane? Why x16?
Q: Would the chipset add latency?
Q: Why is memory b/w in GB/s while PCIe in Gbps
Q: Why is everything other than memory, a serial bus?
Assignment: Why do GPU carry their own memory?
Assignment: How would you think about bandwidth needed to drive a 8k monitor @60Hz (assume 8b each for RGB)? Compare your calculated bandwidth with the spec of the cable you use to connect. How many lanes of PCIe 4.0 would be needed to pump that throughput?
Web server

## Slide 13: Break

## Slide 14: DDR SDRAM
64/72-wide
DDR4-3200
25.6 GB/s
One channel – 64-bit wide
77-wide
Latency – 50ns (because capacitive!)
Memory Controller
DIMM is dumb!
Pure Capacitive Storage
1600 MHz (double data pumping)
@3200 MT/s
Actual throughput achieved?
BURST - throughput hides latency!
Lies?
Notes: What is “Random Access”? What is “Dynamic”? What is “Synchronous”? What is “Double Data Rate”?
Variations in form factor: DIMM, SO-DIMM, LP-DIMM, RDIMM
DDR5 includes on-die ECC, has sub-channels (link ECC in LPDDR5)
Q: Why not go even wider?
Q: Why is memory controller on CPU instead of DRAM sticks?

## Slide 15: Memory Hierarchy
Memory Controller
L3
L1
Register File
L1
Register File
Core 0
Core 1
L2
Register
1 cycle
> 1 TB/s
L1
5 cycles
1 TB/s
L2
15 cycles
1 TB/s
L3
75 cycles
500 GB/s
DRAM
50ns
25 GB/s
2 channels, 64-bit wide
= 128-bit memory bus
= 2x mem bandwidth
Cache
Cache line
(64/128 B)
Throughput hides latency!
Notes: L1i / L1d
Cache line & burst length
Q: Why are L1/L2/L3 faster?
Q: Why measure L1/L2/L3 in cycles, while DRAM in ns? Clocks are different, DRAM number too large.
Q: If L1/L2/L3 are all SRAMs, why do L2 & L3 have higher latency? Higher tag lookups, contention
Q: Where might DCAS be getting implemented?
Q: Do you see why GC languages can be slow?

## Slide 16: Multiple Processors
Memory Controller
Memory Controller
Non-Unified Memory Access
(NUMA)
CPU0
CPU1
UPI/xGMI
Process
Fast
Slow
50 ns
100+ ns
Notes: OS scheduler will be NUMA aware
MESI protocol
Q: UPI vs PCIe

## Slide 17
Raptor Lake Die
Credit: https://en.wikichip.org/wiki/intel/microarchitectures/raptor_lake
Notes: Inter-core interconnect – ring bus

## Slide 18: PCIe
Physical Layer
Data Link Layer
Transaction Layer
RX
TX
CPU
Physical Layer
Data Link Layer
Transaction Layer
RX
TX
Device
1 lane
PIPE
PCIe 4.0 – 16 GT/s
PCIe 5.0 – 32 GT/s
Communication is packetized
16 GT/s = 16 Gb/s = ~2GB/s
Higher latency because serial
Higher Throughput
hides a lot of that latency!
Notes: Technically, not a bus
Packetized - switching
CXL & memory pooling – convergence of memory & I/O
Q: Can a PCIe length be extended forever?
Q: If we’re using x16 lanes, isn’t it “parallel” ?
Q: Why does CPU allow only fixed PCIe configs, e.g. 1x16 + 1x4?

## Slide 19: SATA -> NVMe
SATA Disk
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
NAND
Flash
SATA
NVMe
Storage Medium: Magnetic, Optical, NAND
Protocol: SATA, SAS, NVMe
Form Factor: 2.5”, M.2, U.2
SATA: 32-deep cmd queue, 6 Gb/s
NVMe: 64k queues, 64k-deep cmd/queue
Throughput hides latency!
Speed is governed by both
Notes: Storage Medium: ultimate bottleneck
Protocol: queue depth, latency

## Slide 20
Register
Caches
DRAM
NVMe SSD
HDD
> 1TB/s
1TB/s
25 GB/s /channel @DDR4-3200
0.3ns
1-20 ns
15-90 ns
10-100 us
2-10 ms
Wired LAN @1Gbps?
Wired LAN @10Gbps?
Wifi 6?
DisplayPort?
2+ GB/s
150 MB/s
Notes: Assignment: figure out latency & bandwidth of ones in red.

## Slide 21: Summary
Amdahl’s Law
Performance is all about overall latency
Main memory is damn slow
I/O is muuuuuuch slower
Serial lines rule everywhere, except memory
All of system design is about hiding latency via throughput
  True for hardware, true for software!

## Slide 22: Thank You